## Slide 1: Neutron Detector Array NAND Ambar Chatterjee
All the files used here are available at
http://www.ambar-chatterjee.com
Questions?
DrAmbar@gmail.com
Series of video lectures about ROOT analysis of pre-fission neutrons from the NAND Array at IUAC, New Delhi

## Slide 2
Website: http://www.ambar-chatterjee.com

## Slide 3
NAND ARRAY
100 Liquid Scintillators. 8 rings with angles 9o to 350o
TOF Path 175 cm

## Slide 4
Spherical Scattering Chamber
2 large area MWPCs

## Slide 5: Dividing the MWPC into sections
Since the MWPCs are large, we need to divide MWPC-1 into smaller sections
Some people analyse the data considering only one large section in the centre taking angles based only on the centre point of this section
This is incorrect
If the section chosen is large, the angles will change over different points within the section
If the section chosen is small, we lose statistics (throwing away valuable data)
BAD ANALYSIS
1 large central area
GOOD ANALYSIS
6 Sections
BETTER?
12 Sections

## Slide 6: Calculating Neutron-Fission Angles
for 100 detectors and 6 MWPC sections
There will be 600 neutron spectra from ROOT analysis
Calculation of angles by hand: Difficult for so many cases. Error prone.
Program required.
Easily formulated in terms of 3 dimensional vector geometry

## Slide 7
Define coordinate system with z-axis in the beam direction, y-axis vertical and origin at the target position
x
y
z

## Slide 8
Coordinates of neutron detectors in this frame is available in NAND-Detectors-Sperical.pdf which I am providing. Please change the negative values in this file to positive by adding 360o . Later we will make a text file for use in the analysis.
............... etc ..............

## Slide 9
Now let us look at the XZ plane view of the forward angle MWPC. There is a second MWPC at back angle, centered around the fission folding angle, but we will work out everything in terms of the first MWPC, which we will divide into 6 (or more) sections.
Let denote angle of centre of MWPC with respect to beam (z-axis) and d denote the distance of centre of the MWPC from target. These values will be known from the experimental setup. I have shown the width of the MWPC as 125 mm, it could be different. Let denote the horizontal position and denote the vertical position in the MWPC where the fragment is detected.
View from above looking down
into scattering chamber

## Slide 10
The diagram shows MWPC1 divided into six sections. The central points of each of the 6 sections is indicated.
We will work out based on the and values at the centre of each section of the MWPC. For we will take f2 as emitted at the folding angle direction.
In the experiment and will be derived from the MWPC1 signals:
We will be placing position gates and building coincidence neutron spectra in the ROOT analysis. For each coincidence spectrum we have to work out what are the angles and .

## Slide 11
View from above looking down
into scattering chamber
Transformation of y,d) to (x,y,z) frame
This is not a unit vector, so normalize it
replace by (1)
While calculating for the complementary fragment we will need this unit vector in spherical polar coordinates. Lets keep that ready:
, (2)
If comes negative we have to add 360o
The spherical polar angles of the neutron detector are input. A unit vector in this direction will have rectangular coordinates:
(3)

## Slide 12
The angle between the unit vectors (eqn 1 and 3) is the inverse cosine of the dot product:
Complementary fragment f2
For the complementary fragment we first work out the polar angles of the unit vector along f2 from the folding angle
Then convert this to rectangular:
(4)
and the angle between the unit vectors (eqns 3 and 4) is given by the inverse cosine of the dot product
You will find these equations coded in function Calculate in ThetaSolver4.c
(The other parts of the program are related to the GUI using graphics library GTK4)

## Slide 13
Installing and running ThetaSolver4 in Ubuntu Linux
1. Download ThetaSolver4.c into a working directory
2. Open a terminal in that directory
3. Install the GTK4 graphics library (unless its already installed)
sudo apt install libgtk-4-dev
4. Compile ThetaSolver4:
gcc $(pkg-config --cflags gtk4) -o ThetaSolver4 ThetaSolver4.c $(pkg-config --libs gtk4) -lm
5. Run:
./ThetaSolver4

## Slide 14
The Theta Solver4 Screen
Fill in the inputs and click “Calculate” or run one of the examples

## Slide 15
Example: MWPC1 size 125 mm x 75 mm
In your experiment it could be different.
We can calculate the and d values at the centre of each section as in the table below:
1
2
3
4
5
6
Slice | (mm) | yMWPC (mm)
1 | -41.67 | 18.75
2 | 0 | 18.75
3 | 41.67 | 18.75
4 | -41.67 | -18.75
5 | 0 | -18.75
6 | 41.67 | -18.75
Slice |  | yMWPC (mm)
1 | -41.67 | 18.75
2 | 0 | 18.75
3 | 41.67 | 18.75
4 | -41.67 | -18.75
5 | 0 | -18.75
6 | 41.67 | -18.75
75 mm
125 mm
Example of MWPC1 Geometry
In this example MWPC1 was placed at forward angle 45o wrt beam at a distance of 270 mm (27 cm) from the target. The folding angle from kinematics is 160o

## Slide 16
Lets look at an example:
Fission position slice 2 (, yMWPC= 18.75 mm from the table in previous slide)
Neutron Detector 2306 ring 2 Theta=81.52o Phi=101.9o

## Slide 17
x
y
z
n
f1
Here is what the example looks like.
When you do all the calculations programatically, you dont have to worry about 3D visualisation.

## Slide 18
Program ThetaCalc.c
While ThetaSolver4.c is nice to calculate and check a few cases, its not practical for calculating 600 cases. We need a program which can read the neutron detector geometry file, accept user provided MWPC geometry details and calculate and then write the output over 600 lines so that we can later make use of this file when come to the moving source fit.
So here we present another program ThetaCalc.c
First we need to convert the file NAND-Detectors-Sperical.pdf to a text file so our program will be able to read it.
This is NAND-Detectors.txt (provided on the website).
The program ThetaCalc.c is also provided. It uses the same Calculate() function which you have seen in ThetaSolver4.c
You can compile it with the command:
gcc -o ThetaCalc ThetaCalc.c -lm
and run it with the command ./ThetaCalc

## Slide 19
The program will read the file NAND-Detectors.txt to get for 111 neutron detectors. It will ask the user to provide MWPC1 geometry details and the fission folding angle. It can make either 6 or 12 MWPC slices
Then it will create 666 (111 * 6) or 1332 (111 *12) line output in
Neutron-Fission-Angles.txt
After we have generated about 666 or 1332 neutron spectra using ROOT we can fit all the spectra in one go. The angle data will come from Neutron-Fission-Angles.txt. I will be presenting the program for moving source fit in another video.
By making use of these programs we can easily complete our pre-fission neutron analyis in a matter of minutes. Beginners are initially over-awed when they think they have to first generate then analyse 666 or 1332 spectra for just one beam energy. But I am providing the programs and videos here, which will allow to complete the analysis

## Slide 20
1 slice, 6 slices, 12 or more?
With 16o variation across slices, you can see how bad it is for the moving source fit if we do not slice the MWPC. With 6 slices, the error in angles reduces to 3o and we can reduce this further with 12 slices.
Label | Slice Number |  | 
E4186 | 1 | 113.50 | 79.47
E4186 | 2 | 118.21 | 74.16
E4186 | 3 | 122.38 | 69.21
E4186 | 4 | 119.86 | 72.50
E4186 | 5 | 124.95 | 66.35
E4186 | 6 | 129.39 | 60.40
Label | Slice Number |  | 
E4186 | 1 | 113.50 | 79.47
E4186 | 2 | 118.21 | 74.16
E4186 | 3 | 122.38 | 69.21
E4186 | 4 | 119.86 | 72.50
E4186 | 5 | 124.95 | 66.35
E4186 | 6 | 129.39 | 60.40
At the begining I had indicated that making just 1 slice is bad. 6 slices is better and probably 12 slices still better. Now that we have ThetaCalc.c running, let us look at its typical output Neutron-Fission-Angles.txt for an example case. I show below the 6 the results for one neutron detector with label 4186 which is in Ring4